## Slide 1: Linux UIO Driver for AXI DMA
Yu-Tang Liu
Advisor: Chen-Mou Cheng, Ph.D.
Notes: 0:30

## Slide 2: Outline
Introduction
Linux on FPGA
UIO Driver
Custom IP and DMA
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 3: Outline
Introduction
Linux on FPGA
UIO Driver
Custom IP and DMA
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 4
We want to develop software to control our custom IP with UIO driver in Linux on FPGA.

## Slide 5
We want to develop software to control our custom IP with UIO driver in Linux on FPGA.

## Slide 6: FPGA Board(ZedBoard)
Two parts on FPGA Board
  Programmable Logic (PL)
  Processing System (PS)
Development Tools
  Vivado
  SDK
Notes: Prime: Intuitive, CPUs
Binary: Abstract, ASICs
571: Less Works, Military Observe Topics
5:00

## Slide 7: SDK
Advantage
  Full Suite of Libraries and Device Driver
Disadvantages
  Libraries different Linux Kernel Libraries
  Run Program
=> Linux on FPGA
Notes: Upgrade Protocols
EC Group
ECDLP
7:00

## Slide 8: Outline
Introduction
Linux on FPGA
UIO Driver
Custom IP and DMA
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 9: Linux on FPGA
Required Files
  FSBL
  Bitstream
  U-boot
  Linux Kernel
  Root File System
[13] Y. K. Lee and I. Verbauwhede. A compact architecture for montgomery elliptic curve scalar multiplication processor. In International Workshop on Information Security Applications, pages 115–127. Springer, 2007.
[18] J. López and R. Dahab. Fast multiplication on elliptic curves over gf (2 m) without precomputation. In International Workshop on Cryptographic Hardware and Embedded Systems, pages 316–327. Springer, 1999.
Notes: Omit Y
Steps: 11, 11
Registers: 7, 6
Out-of-Place
10:00

## Slide 10: Example[1]
Boot Linux by SD Card
  Two partition
1st Partition Files
  BOOT.bin
    FSBL + bitstream + u-boot
  uEnv.txt
  uImage
  uramdisk.image.gz
  devicetree.dtb
[1] zedboard-hwswcodesign-example URL https://github.com/concise/zedboard-hwswcodesign-example .
Notes: Omit Y
Steps: 11, 11
Registers: 7, 6
Out-of-Place
10:00

## Slide 11: Device Tree
Non Coverable Device
Old Linux
  Hard Coded
New Linux
  Device Tree
Notes: Omit Y
Steps: 11, 11
Registers: 7, 6
Out-of-Place
10:00

## Slide 13: Outline
Introduction
Linux on FPGA
UIO Driver
Custom IP and DMA
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 14: UIO Driver[]
Suitable
  The device has memory that can mapped and can be controlled by writing to this memory.
  The device usually generates interrupt.
  The device does not fit into one of the standard kernel subsystems.
About UIO
  Main part of driver is developed in userspace.
  Driver won’t crash the kernel.
  Update driver don’t need recompile kernel.
[2] The Userspace I/O HOWTO URL https://www.kernel.org/doc/html/v4.12/driver-api/uio-howto.html .
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 15: Kernel Device Driver UIO Driver
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 16: Outline
Introduction
Linux on FPGA
UIO Driver
Custom IP and DMA
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 17: Custom IP
  Register Types
    Full
    Lite
    Stream
  AXI4 Bus Interface[3]
    AXI4
    AXI4-Lite
    AXI4-Stream
[3] AXI Referenct Guide URL https://www.xilinx.com/support/documentation/ip_documentation/ug761_axi_reference_guide.pdf .
->
->
UIO Driver
->
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 18: Custom Stream IP
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 19: DMA
Direct Memory Access
  Moving data without CPU
  DMA Controller
Usage
  Data Address(Physical)
  Data Length
  Destination Address(Physical)
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 20: DMA Engine
Linux Kernel API[4]
  Request Slave Channel
  Set Channel Parameter
  Get a descriptor for transaction
  Submit the transaction
  Issue pending requests and wait for callback notification
[4] DMA Engine API Guide URL https://www.kernel.org/doc/html/v4.16/driver-api/dmaengine/client.html .
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 21: Outline
Introduction
Linux on FPGA
UIO Driver
Custom IP and DMA
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 22: Linux UIO Driver for AXI4/Lite Custom IP
EX:OpenCores-tinyAES
Devicetree node
  compatible
  reg
  Interrupts
uEnv.txt
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 23: Linux UIO Driver for AXI4/Lite Custom IP
UIO Node
UIO Memory Address
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 24: Linux UIO Driver for AXI4/Lite Custom IP
Code
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 25: Linux UIO Driver for AXI4/Lite Custom IP
Result
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 26: Observation
Device Node
Program
  User-space without Root
  UIO Usage
    open() , mmap()
    Value Assignment
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 27: Linux UIO Driver for AXI DMA
Device Node
  Virtual Device Node
  No Memory Address, Length
  No interrupt
  DMA Informations
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 28: Linux UIO Driver for AXI DMA
Program
  User-space without Root
    Control the DMA Controller directly
    Virtual Memory
  UIO Usage
    How to send transaction?
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 29: Linux UIO Driver for AXI DMA
AXI DMA[5]
  S2MM-Channel
    Steam To Memory Map
  MM2S-Channel
    Memory Map To Steam
[5] AXI DMA URL https://www.xilinx.com/support/documentation/ip_documentation/axi_dma/v7_1/pg021_axi_dma.pdf .
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 30: Linux UIO Driver for AXI DMA
File Operation
  Only open(), mmap()
  UIO read(),write()
  Interrupt control
  Function parameters
uio_read(filep, buf, count, ppos)
uio_write(filep, buf, count, ppos)

## Slide 31: UIO
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 32: UDMA
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 33: Linux UIO Driver for AXI DMA
DMA Issues
  Continuous Memory
    CMA
    Scatter-Gather
      Scatterlist[6]
  Cache Coherency
    Cache Flush
    Cache Invalidable
[6] Scatterlist Chaining URL https://lwn.net/Articles/234617/ .

## Slide 34: UDMA
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 35
Notes: Heuristic: Lazy, Short-Sighted
16:00

## Slide 36: Linux UIO Driver for AXI DMA
EX:OpenCores-tinyAES with DMA
UIO Node
UIO Memory Address
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 37: Linux UIO Driver for AXI4/Lite Custom IP
Code
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 38: Linux UIO Driver for AXI4/Lite Custom IP
Result
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 39: Outline
Introduction
Linux on FPGA
UIO Driver
Custom IP and DMA
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 40: Experimental Results
Other DMA Kernel Drivers
  xilinx_axidma[7] ->CMA
  ezdma[8] -> Scatter-Gather
[7] xilinx_axidma driver URL https://github.com/bperez77/xilinx_axidma.
[8] ezdma driver URL https://github.com/jeremytrimble/ezdma
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 41: Experimental Results
Test IP
  AXI-Stream FIFO
  OpenCores tinyAES with DMA
  ECDSA(curve secp256k1)
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 42: Outline
Introduction
Linux on FPGA
UIO Driver
Custom IP and DMA
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 43: Conclusion
Our Contributions
  Little modification to UIO driver to adapt AXI DMA
  Design an easy way to control AXI4-Stream IP
Future Works
  VDMA, CDMA / Faster / Merge into Linux kernel
Notes: Temporary Records
45:00

## Slide 44: Thanks for your listening!
Yu-Tang Liu
Advisor: Chen-Mou Cheng, Ph.D.