## Slide 1: Linux UIO Driver for AXI DMA
Yu-Tang Liu
Advisor: Chen-Mou Cheng, Ph.D.
Notes: 0:30

## Slide 2: Outline
Introduction
Preliminaries
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Introduction
Background Technology
Mainwork
Test Result
Conclusion
2:00

## Slide 3: Outline
Introduction
Preliminaries
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 4
We want to develop software to control our custom IP with UIO driver in Linux on FPGA.

## Slide 5: FPGA Board(ZedBoard)
Two parts on FPGA Board
  Programmable Logic (PL)
  Processing System (PS)
Development Tools
  Vivado
  SDK
Notes: 講解FPGA有兩個part
PL跟PS端
PL端用VIVADO開發 PS端用SDK開發
5:00

## Slide 6: SDK
Advantage
  Full Suite of Libraries and Device Driver.
Disadvantages
  Libraries are different from Linux Kernel Libraries.
  Run Program.
=> Linux on FPGA
Notes: SDK的好處 在於它提供了很完整的LIB跟DRIVER 讓我們去控制在FPGA端設計出來的硬體
缺點在於 這些LIB跟我們所熟悉的LIB不太一樣 而且在RUN prog的時候很容易出問題
把軟體開發的環境拉回到linux 會是一個不錯的方法
7:00

## Slide 7
We want to develop software to control our custom IP with UIO driver in Linux on FPGA.
Notes: 回到動機 講解UIO driver custom ip的問題

## Slide 8
We want to develop software to control our custom IP with UIO driver in Linux on FPGA.
Notes: 我們提出了一個方法 來解決這個問題

## Slide 9: Outline
Introduction
Preliminaries
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 10: Linux on FPGA
Required Files
  FSBL
  Bitstream
  U-boot
  Linux Kernel
  Root File System
  Device Tree
Notes: FSBL負責把bit 燒進FPGA
並把SSBL load進來 這裡我們用uboot當作SSBL
uboot是我們在嵌入式系統常常用到的bootloader 用來load linux kernel
10:00

## Slide 11: Device Tree
Non Coverable Device
Old Linux
  Hard Coded
New Linux
  Device Tree
FPGA
  devicetree.dts (default) + devicetree.dtsi (PL design)
Notes: Devietree機制
在FPGA板子中 可以理解為dt.dts + dt.dtsi 其中dtsi的部分為PL端設計所多出來的硬體

## Slide 12: UIO Driver[1]
Suitable
  The device has memory that can be mapped and can be controlled by writing to this memory.
  The device usually generates interrupt.
  The device does not fit into one of the standard kernel subsystems.
About UIO
  Main part of driver is developed in userspace.
  Driver won’t crash the kernel.
  Update driver don’t need recompile kernel.
[1] The Userspace I/O HOWTO URL https://www.kernel.org/doc/html/v4.12/driver-api/uio-howto.html .
Notes: UIO driver
適用於那些裝置 以及特色
13:00

## Slide 13: Kernel Device Driver UIO Driver
Notes: Kernel device driver vs uio driver
13:00

## Slide 14: Custom IP
Register Types
  Full
  Lite
  Stream
AXI4 Bus Interface[2]
  AXI4
  AXI4-Lite
  AXI4-Stream
[2] AXI Referenct Guide URL https://www.xilinx.com/support/documentation/ip_documentation/ug761_axi_reference_guide.pdf .
[3] AXI Protocol URL http://www.googoolia.com/wp/wp-content/uploads/2014/04/axi_stream.pdf
->
->
UIO Driver
->
[3]
Notes: Regitster types in Vivado design
Three types vs three protocol
13:00

## Slide 15: Example[4]
Boot Linux by SD Card
  1st partition: boot files
  2nd partition: file system
1st Partition Files
  BOOT.bin
    FSBL + bitstream + u-boot
  uEnv.txt
  uImage
  uramdisk.image.gz
  devicetree.dtb
[4] zedboard-hwswcodesign-example URL https://github.com/concise/zedboard-hwswcodesign-example .
Notes: Simple example: uio driver for axi/lite custom ip
10:00

## Slide 16: Linux UIO Driver for Full/Lite Custom IP
EX:OpenCores-tinyAES[5]
Devicetree node
  compatible
  reg
  Interrupts
uEnv.txt
[5] OpenCores tinyAES URL https://opencores.org/project/tiny_aes .
Notes: Opencore tinyaes 128 12reg 8+4
Device node of custom ip
Compatible = of_id
13:00

## Slide 17: Linux UIO Driver for Full/Lite Custom IP
UIO Node
Notes: Uio node under /dev/
13:00

## Slide 18: Linux UIO Driver for Full/Lite Custom IP
Code
Notes: Example c code of using UIO driver
13:00

## Slide 19: Linux UIO Driver for Full/Lite Custom IP
Result
Notes: Testing result
13:00

## Slide 20: Observation
Device Node
  DMA Controller node
  No custom IP node.
Notes: Device node of axi stream ip
13:00

## Slide 21: Full/Lite Custom IP v.s Stream Custom IP
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 22: Outline
Introduction
Preliminaries
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 23: DMA
Direct Memory Access
  Moving data without CPU.
  DMA Controller
Usage
  Data Address(Physical)
  Data Length
  Destination Address(Physical)
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 24: DMA Engine
Linux Kernel API[6]
  Request Slave Channel.
  Set Channel Parameter.
  Get a descriptor for transaction.
  Submit the transaction.
  Issue pending requests and wait for callback notification.
[6] DMA Engine API Guide URL https://www.kernel.org/doc/html/v4.16/driver-api/dmaengine/client.html .
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 25: AXI DMA[7]
Two Unidirectional Channels
  S2MM-Channel
    Stream To Memory Map
  MM2S-Channel
    Memory Map To Stream
  Data Address
  Data Length
  Destination Address
[7] AXI DMA URL https://www.xilinx.com/support/documentation/ip_documentation/axi_dma/v7_1/pg021_axi_dma.pdf .
Notes: AXI DMA = DMA Contoller
13:00

## Slide 26: Problem
Device Node
  Only DMA Controller Node.
  No UIO device node.
Program(User-space without Root)
  How to send DMA transaction?
Notes: Need device node to bind with driver
How to send transaction?
13:00

## Slide 27: Linux UIO Driver for AXI DMA
Device Node
  Virtual device node.
  No register address, length.
  No interrupts.
  DMA information.
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 28: Linux UIO Driver for AXI DMA
Program
  User-space without Root
    Control the DMA Controller directly.
    Virtual Memory
  DMA Usage
    CMA
    Scatter-Gather
      Scatterlist[8]
[8] Scatterlist Chaining URL https://lwn.net/Articles/234617/ .
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 29: Linux UIO Driver for AXI DMA
File Operation
  UIO read(),write()
  Interrupt Control
  Function Parameters
read(filep, buf, count)
write(filep, buf, count)

## Slide 30: Linux UIO Driver for AXI DMA
DMA Issues
  Cache Coherency
    Cache Invalid
    Cache Flush

## Slide 31: UIO
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 32: UDMA
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 33: UDMA
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 34: Outline
Introduction
Preliminaries
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 35
Notes: Boot files after modification
16:00

## Slide 36: Linux UIO Driver for AXI DMA
EX:OpenCores-tinyAES with DMA
UIO Node
Notes: Same example
13:00

## Slide 37: Linux UIO Driver for AXI DMA
Code
Notes: Usage of our driver
13:00

## Slide 38: Linux UIO Driver for AXI DMA
Result
Notes: ECC Small Instances
500 Variables, 8000 Equations
13:00

## Slide 39: Experimental Results
Other DMA Kernel Drivers
  xilinx_axidma[9] ->CMA
  ezdma[10] -> Scatter-Gather
[9] xilinx_axidma driver URL https://github.com/bperez77/xilinx_axidma.
[10] ezdma driver URL https://github.com/jeremytrimble/ezdma
Notes: No other uio modification
Compare with kernel driver
13:00

## Slide 40: Experimental Results
Experiment Environment
  Platform : ZedBoard
  Linux Kernel : 4.9.9
  Vivado & SDK Version : 2016.04
  Booting Linux from SD card
Notes: Test environment
13:00

## Slide 41: Experimental Results
Test IP
  AXI-Stream FIFO
  OpenCores tinyAES with DMA
  ECDSA(curve secp256k1)
Notes: AXI-stream fifo
Opencore …
Ecdsa curve secp 256k1
Average 1000000 times
13:00

## Slide 42: Outline
Introduction
Preliminaries
Linux UIO Driver for AXI DMA
Experimental Results
Conclusion
Notes: Motivation, Strategy, Preliminaries
Scheduler
Comparison, Simulation
Processor, System
Contribution, Future
2:00

## Slide 43: Conclusion
Our Contributions
  Modify UIO driver slightly to adapt AXI DMA.
  Design an easy and intuitive way to control AXI4-Stream IP.
  Not bad throughput.
Future Works
  VDMA, CDMA / Faster / Merge into Linux kernel.
Notes: Temporary Records
45:00

## Slide 44: Thanks for your listening!
Yu-Tang Liu
Advisor: Chen-Mou Cheng, Ph.D.